## Slide 1: Antenna Modeling Demo
Jim McCusker – K3YO
March 9, 2022

## Slide 2: Antenna Modeling
Most modeling software is based on NEC (Numerical Electromagnetics Code)
  Developed in Fortran in 1970’s
  Most of todays modeling software is derivative of the original code
  Developed by Gerald Burke & Andrew Poggio of the Lawrence Livermore National Laboratory.
NEC software archive: https://www.pa3kj.com/nec-archives/

## Slide 3: Popular NEC Antenna Modeling Software
EZNEC (PC, free) – https://eznec.com/
  AutoEZ ($79) - http://www.ac6la.com/autoez.html
MMANA-GAL (PC) - http://gal-ana.de/
cocoaNEC 2.0 (Mac) - http://www.w7ay.net/site/Applications/cocoaNEC/
YagiCAD - https://www.yagicad.com/
YAGio - https://wb0dgf.com/Yagio.html
NEC2GO - https://www.nec2go.com/

## Slide 4: EZNEC
One of the most widely used antenna modeling programs
Great documentation – (you must RTFM)
Lots of public (.EZ) files you can download and play with
  http://www.nic.funet.fi/pub/ham/antenna/NEC/EZNEC_FILES/
  http://www.arrl.org/antenna-modeling-files
Most important, it’s FREE!!
  Author, Roy Lewallen (W7EL) officially retired January 1, 2022
  Absolutely no software support moving forward
  Source code will never be released

## Slide 5: Get on with the DEMO already!

## Slide 7: Delay Line Calculation
Ideal: wavelength * (phase shift in degrees/360)
Proper: wavelength (in cable) * (phase shift in degrees/360)
Final: ((Vf) x c / freq) x (phase shift in degrees / 360)
Coax Delay Length (TL/DR): https://electronics.stackexchange.com/questions/197900/how-to-determine-length-of-coax-to-get-a-certain-delay